## Slide 1: Tropos field area networks
for smart grid applications
November 2013

## Slide 2: Agenda
Tropos overview
Where we fit in the overall communications architecture
Key architectural choices/alternatives
  Broadband vs narrowband
  Public vs private
  Licensed vs unlicensed
  PTMP vs mesh
What the key challenges are:
  Reliability, range, security, TCO
Discussion: Where technology is headed:
  New spectrum: TVWS, 3.65 GHz, 700 MHz, 5GHz
  New RAN technologies: LTE, 802.11ac, 802.15.4g, MIMO

## Slide 3: Tropos mesh network overview
Founded 2000, acquired by ABB in 2012
Products: Mesh routers, directional radios, network management
Attributes: High capacity, low latency, reliable, secure, adaptable
Field-proven success:
  Installed for 10+ years, acquired by ABB in 2012
  850+ customers in 50+ countries
  60,000+ installed routers
Customers: utilities, oil and gas, mining, public safety, military and industrial applications
Wireless IP networks for mission-critical applications

## Slide 4: What Tropos provides
A cost-effective, standards-based wireless IP network communications system
  Hardware, software, management and analysis tools
  Ruggedized, weatherized equipment
  Carrier-class management
  Enterprise-class security
An enabler for a diverse set of applications
  Hundreds of applications over one network
  Provides capacity for future applications
  IP-based applications ease rollout
  Field automation, SCADA, security and surveillance, mobile workforce

## Slide 5: Where Tropos fits
November 2013

## Slide 6: Applications Drive Bandwidth Requirements
Other high traffic applications
  Substation Video
  PHEV Station
  Mobile GIS
  AVL
  …and more in the future

## Slide 7: Higher tiers require more aggregate bandwidth
Same as enterprise networks

## Slide 8: Tropos Distribution Area Network

## Slide 9: Keys to successful field area networks
Standards-based
  TCP/IP, 802.11, 802.3 Ethernet, 802.1x….
  Legacy protocol support: serial links, DNP3…
High bandwidth & low latency
  > 10 Mbps throughput at each node, < 1 ms latency per hop
Resilient
  Self-organizing mesh, hardened equipment, can deliver > 99.999% system availability
Secure
  Multi-layer/multi-application model, enterprise-class
Manageable
Scalable to economically cover small areas to thousands of square miles

## Slide 10: Competitive landscape
Commercial cellular data services
Broadband mesh networks
  Multi-application networks for DA, AMI backhaul, mobility
AMI metering networks
  Low bandwidth, long latency networks, typically mesh
Broadband PTP/PTMP
  Substation capacity, capacity injection into mesh networks (AMI and broadband), direct connectivity to DA devices
Narrowband PTP/PTMP
  Low bandwidth, low latency, long range connectivity to sparse assets: AMI collectors, DA devices
Five competitive smart grid communications architectures
Broadband PTP/PTMP
DA
Capacity
Broadband Mesh
Narrowband PTP/PTMP
AMI Mesh

## Slide 11: Architectural choices: Narrowband vs Broadband
November 2013

## Slide 12: Selecting a network communications strategy
Traditional approach
Network per project
  Build/pay as you go
SCADA
Distribution automation
Telemetry
Field data applications,…
Strategic approach
Layered communications architecture
Supports for current plus future applications
Minimizes incremental spend for additional field applications
Leverages standards to make application roll out easier

## Slide 13: Smart Networks fundamental to Smart Grid
Source: AEP
AMI
Initial Capital Outlay
Meter functionality
Communications infrastructure
Head-end & legacy systems modifications
Incremental Capital Commitment
Expected Value
Demand Response
Distribution Operations & Automation
Extended Utility Roles

## Slide 14: Architectural choices: Mesh vs Cellular
November 2013

## Slide 15: Cellular vs. private networks
Metric | Cellular | Private Network
Availability | Moderate-high availability | Can be designed to be very high availability (five nines)
Survivability | OK for non-critical data transport, inadequate for mission-critical apps | Highly survivable architectures and technology options
Coverage | Limited coverage in rural/lightly-populated areas | Can be engineered to very high levels, but requires mix of technologies
Latency | 100-1000 ms | 10-100 ms
Security | Adequate | Highly secure options exist

## Slide 16: In many situations, private is strongly preferred
Coverage: Environments that have to build private networks because of lack of cellular coverage
  Remote locations (mines, ships, oil rigs, rural area), indoors (industrial)
Performance: Where application performance needs can not be met by public cellular network
  Demanding applications: low latency DA (reclosers, sectionalizers, automated feeder reconfig)
  Mission-critical apps that require QoS and prioritized access
Cost: Where private offers a less expensive solution
  Rate structure favors capital spend over Opex
  Public cellular data pricing is high and/or unpredictable
  Large number of devices and/or apps makes private cheaper
Other: Other segments which prefer private to public when both are viable options
  In substation or industrial setting where 802.11 exists
  Customer desires complete control with no dependence on public infrastructure

## Slide 17: Public vs. private networks
Competing approaches, but can also be complementary to a great extent. For example:
  Private mesh networks can extend the coverage of cellular and fill in dead spots
  Communications nodes can leverage multiple uplinks for failover
Utilities are continuing to use public networks for
  Non-mission-critical applications (AMI backhaul, …)
  Point applications
  Fill-in for coverage where it may not be economical to build private networks
Utilities tend to prefer private networks, especially where
  Mission-critical apps have stringent performance and reliability requirements
  Network is viewed as a common foundation for multiple smart grid applications
Summary
Notes: Cellular is a good fit for certain applications and use cases - for example AMI backhaul. It is less of a fit for mission-critical apps that need high reliability and high performance. Utilities have used cellular in their comms networks and will probably continue to do so.
Private network technologies offer much higher levels of reliability and performance and offer utilities a lot more control. Much better fit for mission-critical apps. Also, makes more economic sense when the network is viewed not just as a solution to a tactical problem of transporting data for a specific application, but rather as the strategic asset underpinning multiple applications that the utility will deploy over the next 15-20 years.

## Slide 18: Architectural choices: Licensed vs Unlicensed
November 2013

## Slide 19: Comparing licensed and unlicensed spectrum
 | Exclusively Licensed Spectrum | Lightly Licensed Spectrum | Unlicensed Spectrum
Cost |  |  | 
Availability |  |  | 
Performance |  |  | 
Interference |  |  | 
Security |  |  | 
Interoperability |  |  | 
Poor
Best

## Slide 20: Architectural choices: Broadband mesh vs AMI mesh
September 2012

## Slide 21: Bandwidth and latency
Requirements vs. performance
Latency
Throughput / device
bps
Mbps
Kbps
1 msec
100 msec
>5 sec
1 sec
AMI
AMI
BH
Res
DR
Protect
Video
Volt VAR
Cont
Mobile
WF
Broadband Mesh Performance
AMI Mesh Performance

## Slide 22: Architectural choices: Mesh vs Broadband PTMP
November 2013

## Slide 23: Mesh architectures and applications
Mesh architectural attributes:
  Self-organizing  military ad hoc networks
  Resilient and self-optimizing  High-reliability mission-critical communications in private networks
  High capacity  densified small cells (WiFi or LTE) for scaling mobile data capacity
  Fractional backhaul  cost-effective solution where supporting wired infrastructure is minimal/expensive

## Slide 24: Redundant paths, channels and bands
Tropos Mesh OS leverages multiple paths, channels and bands to create robust, high performance networks
MESH NODE
MESH NODE
MESH NODE
MESH NODE
MESH NODE
MESH NODE
MESH NODE
MESH NODE
MESH NODE
MESH NODE
MESH NODE
MESH NODE
MESH NODE
MESH NODE
Optimal routing paths
Backup links
Wired backhaul
  2.4 GHz Link
  5.X GHz Link
Mesh links dynamically choose 5 GHz or 2.4 GHz band
Channel within band automatically chosen on a per link basis
Notes: 24

## Slide 25: PTMP and Mesh are Complementary
Pont-to-multipoint (PTMP) and Mesh are complementary technologies for the DAN layer
  PTMP is very cost-effective for suburban and rural deployments and for mesh capacity injection in denser areas
  Mesh is well-suited for urban areas providing resilience and higher capacity
Optimal combination of Mesh and PTMP leverages the strengths of both
  Mesh extends coverage range of PTMP and improves reliability
  Architectural resilience through mesh failover capabilities
  Combined deployment achieves
    Economics optimized for mix of urban/suburban/rural areas
    Meets requirements for multiple DAN applications

## Slide 26: GridCom Architecture: Mesh + PTMP
Increase System Availability (>99.99%)
With Tropos Mesh Routing Technology
Eliminate PTMP Shadowing (Route around obstacles)
5 mile radius  10+ mi radius
78.5 sq miles  300 to 1,000+ sq miles
3 to 10 x coverage per tower
Expand PTMP Cell Radius
With Combination of PTMP + Tropos
Reduce #
of Towers
10+
5

## Slide 27: What Mix of Mesh and PTMP Looks Like
Data Center(s)
Tropos
Control
Tier 3 (NAN)
Tier 4 (HAN)
Dense
Urban
Urban
Suburban
Rural / Ultra Rural
Tier 1: Fiber (SONET, GigE), Microwave, MPLS Core
Decreasing Mesh Density
Transition to WiMAX/P2MP/LTE
Tier 1 Topology Implemented with
Path Diversity Where Possible
Spur
Fiber
Microwave
Tropos Gateway (GW)
Routers Installed at
Tier 1 Core Sites
GW
GW
GW
P2MP Demarc to
Mesh Gateways
Tropos Node (ND) Routers
Distribute Tier 2
Capacity Across
Urban/Suburban
Service Areas
Smart Grid Devices
Connect via Wired
or Wireless Ethernet
to Tropos Mesh Nodes
Tier 1 / Tier 2
Mesh Used in Rural
to Overcome P2MP
Propagation Obstacles
Rural Subscribers
Served via P2MP

## Slide 28: Summary
November 2013

## Slide 29: Keys to successful field area networks
Standards-based
  TCP/IP, 802.11, 802.3 Ethernet, 802.1x….
  Legacy protocol support: serial links, DNP3…
High bandwidth & low latency
  > 10 Mbps throughput at each node, < 1 ms latency per hop
Resilient
  Self-organizing mesh, hardened equipment, can deliver > 99.999% system availability
Secure
  Multi-layer/multi-application model, enterprise-class
Manageable
Scalable to economically cover small areas to thousands of square miles

## Slide 30: Where technology is headed
November 2013

## Slide 31: Field automation communication challenges
Reliability of connections
Network capacity headroom to enable future applications
Low latency to support automation applications
Support multiple applications with QoS, security and traffic segmentation
Scalable to large number of devices covering large geographic areas
Cost-effective
Easy interoperability with edge devices, avoid stranded assets
Communicate with thousands of endpoints in large geographic areas

## Slide 32: Research Themes
Interference mitigation
Longer range
System cost
Cybersecurity
Heterogeneous networks
Ease of installation and management
Smaller footprint endpoints (lower power consumption, lightweight routing stack, lower cost radios)
Heavily loaded networks

## Slide 33: Tropos field area networks
for smart grid applications
November 2013